## Slide 1: CCNA 200-301
Implementing OSPF

## Slide 2: Objectives
Implementing Single-Area OSPFv2
OSPFv2 Interface Configuration
Additional OSPFv2 Features

## Slide 3
Step 1. Use the router ospf process-id global command to enter OSPF configuration mode for a particular OSPF process.
Step 2. (Optional) Configure the OSPF router ID by doing the following:
  A. Use the router-id id-value router subcommand to define the router ID.
  B. Use the interface loopback number global command, along with an ip address address mask command, to configure an IP address on a loopback interface (chooses the highest IP address of all working loopbacks).
  C. Rely on an interface IP address (chooses the highest IP address of all working nonloopbacks).
Step 3. Use one or more network ip-address wildcard-mask area area-id router subcommands to enable OSPFv2 on any interfaces matched by the configured address and mask, enabling OSPF on the interface for the listed area.
Step 4. (Optional) Use the passive-interface type number router subcommand to configure any OSPF interfaces as passive if no neighbors can or should be discovered on the interface.
Implementing Single-Area OSPF

## Slide 4
Implementing Single-Area OSPF

## Slide 5: Sample Network for OSPF Single-Area Configuration

## Slide 6: IPv4 Address Configuration on R1 (Including VLAN Trunking)

## Slide 7
The router ospf 1 global command puts the users into OSPF configuration mode and sets the OSPF process-id to 1.
This process-id just needs to be unique on the local router and be between 1 and 65,535.
The OSPF network command tells the router to find its local interfaces that match the first two parameters in the command.
Those interfaces then discover neighbors, create neighbor relationships and assign the interface to the area listed.
Implementing Single-Area OSPF

## Slide 8
The wildcard mask gives the local router its rules for matching its own interfaces:
  Wildcard 0.0.0.0: Compare all 4 octets. In other words, the numbers must exactly match.
  Wildcard 0.0.0.255: Compare the first 3 octets only. Ignore the last octet when comparing the numbers.
  Wildcard 0.0.255.255: Compare the first 2 octets only. Ignore the last 2 octets when comparing the numbers.
  Wildcard 0.255.255.255: Compare the first octet only. Ignore the last 3 octets when comparing the numbers.
  Wildcard 255.255.255.255: Compare nothing—this wildcard mask means that all addresses will match the network command.
Matching with the OSPF network Command

## Slide 9
Matching with the OSPF network Command

## Slide 10
Matching with the OSPF network Command

## Slide 11: OSPF Verification Commands

## Slide 12
Interface: This is the local router’s interface connected to the neighbor. For example, the first neighbor in the list is reachable through R3’s S0/0/0 interface.
Address: This is the neighbor’s IP address on that link. Again, for this first neighbor, the neighbor, which is R1, uses IP address 10.1.13.1.
State: While many possible states exist, for the details discussed in this chapter, FULL is the correct and fully working state in this case.
Neighbor ID: This is the router ID of the neighbor.
Verifying OSPFv2 Single Area

## Slide 13
When OSPF is working correctly in the internetwork with a single-area design, all of the routers will have the same LSDB contents.
For the purposes of the CCNA knowledge of the specifics about the output of this command are not required.
Verifying OSPFv2 Single Area

## Slide 14
IPv4 Routes Added by OSPF

## Slide 15: Router R3 Configuration and the show ip protocols Command

## Slide 16: show ip ospf interface brief Command

## Slide 17
OSPF speaking routers must have a router-ID (RID) for proper operation.
By default, routers will choose an interface IP address to use as the RID.
Typically, engineers prefer to choose each router’s RID.
A Cisco router uses the following process when the router reloads and brings up the OSPF process to find the RID:
  If the router-id rid OSPF subcommand is configured, this value is used as the RID.
  If any loopback interfaces have an IP address configured, and the interface has an interface status of up, the router picks the highest numeric IP address among these loopback interfaces.
  The router picks the highest numeric IP address from all other interfaces whose interface status code (first status code) is up. (In other words, an interface in up/down state will be included by OSPF when choosing its router ID.)
Configuring the OSPF Router ID

## Slide 18
OSPF Router ID Configuration Examples

## Slide 19: Implementing Multiarea OSPF

## Slide 20: OSPF Single-Area Configuration

## Slide 21: OSPF Single-Area Configuration

## Slide 22
An OSPF interface configured as passive will do the following:
  Quit sending OSPF Hellos on the interface.
  Ignore received Hellos on the interface.
  Do not form neighbor relationships over the interface.
OSPF does not form neighbor relationships over interfaces configured as passive, but does still advertise about the subnet connected to that interface.
OSPF Passive Interfaces

## Slide 23
To configure an interface as passive there are two options:
  Adding the passive-interface type number command under router configuration mode.
  Configuring interfaces as passive by default with the passive-interface default command under global configuration mode and using the no passive-interface type number command to disable passive of specific interfaces.
OSPF Passive Interfaces

## Slide 24
OSPF makes it interesting to figure out which interfaces are passive:
  The show ip ospf interface brief command lists all interfaces on which OSPF is enabled including passive interfaces.
  The show ip ospf interface command lists a single line that mentions that the interface is passive.
OSPF Passive Interfaces

## Slide 25
The most classic case for using a routing protocol to advertise a default route has to do with an enterprise’s connection to the Internet.
The enterprise engineer uses the following design goals:
  All routers learn specific routes for subnets inside the company; a default route is not needed when forwarding packets to these destinations.
  One router connects to the Internet, and it has a default route that points toward the Internet.
  All routers should dynamically learn a default route, used for all traffic going to the Internet, so that all packets destined to locations in the Internet go to the one router connected to the Internet.
OSPF Default Routes

## Slide 26
R1 has a static default route with a next-hop address of the ISP router.
R1 uses the OSPF default-information originate command to advertise a default route using OSPF to B1 and B2.
R1 needs a default route, either defined as a static default route, learned from the ISP with DHCP or learned from the ISP with a routing protocol like eBGP unless the always parameter is used.
OSPF Default Routes

## Slide 27
The branch routers then place the learned OSPF default route into their routing tables.
OSPF Default Routes

## Slide 28
R1 uses DHCP to learn its IP address on its Gi0/3 interface from the ISP.
R1 then creates a static default route with the ISP router’s IP address of 192.0.2.1 as the next-hop address.
OSPF Default Routes

## Slide 29
Cisco routers allow three different ways to change the OSPF interface cost:
  Directly, using the interface subcommand ip ospf cost x.
  Using the default calculation per interface, and changing the interface bandwidth setting, which changes the calculated value.
  Using the default calculation per interface, and changing the OSPF reference bandwidth setting, which changes the calculated value.
IOS uses the Reference_bandwidth / Interface_bandwidth formula to choose an interface’s cost.
With this formula the following sequence of logic happens:
  A higher interface bandwidth—that is, a faster bandwidth—results in a lower number in the calculation.
  A lower number in the calculation gives the interface a lower cost.
  An interface with a lower cost is more likely to be used by OSPF when calculating the best routes.
OSPF Metrics (Cost)

## Slide 30
OSPF Metrics (Cost)

## Slide 31
OSPF Metrics (Cost)

## Slide 32
Typically when SPF calculates the metric of several routes, one route will have the lowest metric, so OSPF puts it into the routing table.
When metrics tie for multiple routes to the same subnet, the router can put multiple equal-cost routes into the routing table. (By default, up to 4.)
This default can be altered with the maximum-paths number command.
Routers can load balance in one of two ways:
  On a per-packet basis, where each new packet it forwarded out the next path in round robin.
  On a per-destination bases, where packets are forwarded using the same path for each specific IP destination.
OSPF Load Balancing